## Slide 1: Data-Driven Optimization and Fault Detection in Solar Power Plants
CIVE70111 - Machine Learning
Group 11
12/12/2025

## Slide 2: Scope and Objectives
What is the problem? Why do we need to solve it? How to solve it?
Raw Data
Propressing
Regression
Classification
Insights
Challenge
Solar energy is intermittent and weather-dependent, making it hard for grid operators to balance supply and demand.
Solution
Accurate forecasting to ensure grid stability and fault detection to minimize downtime.
Power Forecasting
1. Predict DC Power output for the next period.
2.Helps plan energy dispatch
Fault Detection
1. Identify inverters that are underperforming
2. Enables predictive maintenance and reduces loss
Data Mining Pipeline
1. Data Cleaning
2. Feature Engineering
3. Model Training
4. Evaluation.
Task
Performance
Experience

## Slide 3: Scope and Objectives
Task
Performance
Experience

## Slide 4: Task 3
Data Ingestion
Loaded raw CSV files
Fix timestamp formats, remove invalid rows utlier Detection
Clean Data & Outlier Detection
Check for missing values and duplicates
Remove high‑residual (z > 3) points
Aggregate & Merge
Combine inverter readings with weather by timestamp
Links specific power output to the exact weather conditions
EDA & Visualization
Calculated Correlation Matrices and visualized Time-Series Plots.
Visualized the "Bell Curve" of daily production
Objective
Conduct an exploratory analysis of the power generation and sensor data, derive insights to inform modelling decisions, and prepare for machine learning.
Workflow Overview

## Slide 5: Task 2 Results
Irradiation is the main driver.
Correlation Matrix confirms a positive correlation (0.98) between Irradiation and DC Power.
Module_Temperature is the secondary factor
Shows a strong correlation with power (0.95), higher than Ambient_Temperature, indicating that the panel's internal temperature is a more relevant feature than the surrounding air temperature.
Key insights from Data
3. Linearity
The data points form a tight, linear cluster extending from the origin, confirming the strong physical relationship identified in the heatmap
4. Daily cyclical pattern
Shows a daily cyclical pattern in power generation.This observation justifies the feature engineering step where
we extracted the 'Hour' component from the timestamp
Temporal Dynamics: Verification of Daily Solar Cycles
Key Predictors Correlation Heatmap
Scatter Plot: Irradiation vs. DC Power

## Slide 6: Introduction to Task 3
Objectives
Develop models to forecast the power output using environmental conditions to anticipate power production capabilities and optimize.
Feature Selection & Data Splitting
Selected Irradiation, Ambient Temperature, Module Temperature as predictors.
Split each inverter into one CSV per day
Performance Evaluation
Calculated RMSE, MAE and R² for DC & AC power.
Compare model Bias–variance, performance & stability
Modeling Training
Linear Regression
Neural Network
Lasso Regression
Ridge Regression
Random Forest
Neural Network Analysis and Operational Visualisation
Visualise DC & AC loss curves
Compute convergence speed, iterations, training time
Time‑of‑day performance plots
Workflow Overview

## Slide 7: Task 3 Results
Performance & Insights
Bias-Variance Analysis using RMSE Proxies
Five different models been trained for comparison.
Distribution of RMSE across 22 Inverters
Deviation & Variance | 
 | Random Forest shows the smallest value
 | Random Forest has the best accuracy and stability
RMSE in all inverters | 
 | Random Forest shows the narrowest distribution
 | Random Forest model performs consistently well across different hardware

## Slide 8: Introduction to Task 4
Objective
Detect suboptimal inverter operating conditions in solar plants using interpretable, data‑driven machine learning models.
Data Loading & Cleaning
Import inverter + weather data (Plant 1 & 2).
Fix timestamps, clean AC/DC power, yields, and irradiation.
Remove outliers via regression residual analysis.
Time‑Based Splitting
Chronological train /
validation / test split
→ prevent leakage.
Feature Engineering
Compute ratios: AC/IRRA, DC/IRRA.
Add temperature + yield features.
Label target: Optimal (0) / Suboptimal (1).
Interpretability
ALE plots → feature impact direction.
Drop‑Column Importance → quantify feature contribution.
Model Training
Models: Logistic Regression & Linear SVC
(with & without scaling).
Balanced class weights; F1‑optimised thresholds for suboptimal detection.
Workflow Overview
Experiments
With / without outlier removal.
Before / after feature selection.
Compare Plant 1 vs Plant 2.
Key Takeaway
Feature Scaling improves all models.
Feature Selection (Drop‑Column) enhances stability & interpretability.
Outlier Removal did not improve performance — some were valid points.

## Slide 9: Task 4 Results
Experiments : Plant 1
Before feature selection vs After feature selection
With outliers vs Without outliers
Condition | Outliers | Feature Selection | Accuracy | Macro F1 | Analysis
1. Before feature selection | ✅ Included | ❌ No | 0.989–0.990 | ≈ 0.974–0.975 | Excellent results; model predicts both classes well
2. After feature selection | ✅ Included | ✅ Yes | 0.990 | ≈ 0.975 | Almost identical to before; feature removal did not affect much
3. Before feature selection | ❌ Removed | ❌ No | 0.991–0.992 | ≈ 0.975–0.979 | Still very high, but recall slightly improved due to data cleaning
4. After feature selection | ❌ Removed | ✅ Yes | 0.989–0.991 | ≈ 0.971–0.975 | Small drop — less diverse data and fewer features slightly reduced precision
ALE plots for feature selection
SVM decision function

## Slide 10: Introduction to Task 5
Objective
Interpret Random Forest models for DC and AC power prediction.
Identify key features influencing PV output (irradiation, temperature, time‑of‑day).
Compare Plant 1 vs Plant 2 and extract physical/operational insights.
Workflow Overview
Key Takeaway
Permutation Importance – used to catch few important features.
SHAP – feature‑level contribution to predictions.
PDP – global relationship between features and output.
Data Loading & Cleaning | Combine inverter CSVs, filter dates, fill gaps.
Feature Engineering | Create irradiation, temperature, yield, and time‑of‑day features.
Train Models | Random Forest regressors for DC and AC outputs.
Interpret Models using | Permutation Importance (global ranking) SHAP Waterfall Plots (local effects) Residualisation Coefficients (feature sensitivity) PDP & PDP Slopes (average feature influence)
Output | Visualize & Compare results for both

## Slide 11: Task 5 Results
Permutation Importance
the feature of model strongly depends on.
SHAP Waterfall Plot
higher sunlight drastically raises AC power.
PDP-Based Importance
strongest effect on output. ( uses as coefficient)

## Slide 12: Introduction to Task 6
Objective
Analyze and model two PV plants to:
Classify operation as Optimal/Suboptimal (Linear SVC).
Forecast AC/DC power 1 hour ahead (PyTorch LSTM).
Workflow Overview
Loading Data:
Load CSV files for each plant
Merge data on timestamp and source key (inverter ID)
Convert timestamps to a uniform timezone (15‑min interval assumed)
Data Cleaning & Validation
Timestamp cleaning
Irradiance correction
Remove negatives/outliers
Replace missing data with interpolation (time‑based).
Fix cumulative yields
For each inverter, generate clean sub‑DataFrames.
Feature Engineering
Compute power‑to‑irradiance ratios
Compute temperature difference
Extract time features
Normalize column naming with suffix
Forecasting (LSTM)
Create sequences:
Train/validation/test split
chronologically.
Normalize features:
Model design
Training
Evaluate
Key Takeaway
Built an end‑to‑end ML pipeline for PV plants.
Linear SVC → classifies Optimal vs Suboptimal operation.
LSTM → forecasts AC/DC power 1 hour ahead.

## Slide 13: Task 6 Results
Classification (Linear SVC)
Plant | Optimal | Suboptimal | Threshold | PR‑AUC | Accuracy | F1 (Suboptimal) | Remarks
Plant 1 | 7 656 | 38 024 | 0.0065 | 1.0000 | 99.0 % | 0.994 | Excellent separation; almost perfect recall (1.0)
Plant 2 | 7 414 | 60 284 | 0.7671 | 0.9987 | 96.0 % | 0.978 | Very high precision/recall; mild false positives
Key Takeaway
Both plants show exceptional classifier performance, reliably identifying suboptimal operation with nearly perfect PR‑AUC and F1 scores.
2. Forecasting (LSTM vs Baselines)
Plant | LSTM_MAE | LSTM_RMSE | Persistence_MAE | Persistence_RMSE | MA_MAE | MA_RMSE | Winner
Plant 1 (AC) | 86.9 | 135 | 96.6 | 171 | 117.9 | 189 | LSTM (by ~10 MAE ↓)
Plant 2 (AC) | 888.7 | 1 390 | 988.4 | 1 755 | 1 207 | 1 935 | LSTM (by ~10 % better)
Plant 1 (DC) | 97.0 | 146 | 98.2 | 169 | 106.3 | 171 | LSTM slightly better
Plant 2 (DC) | 94.6 | 147 | 100.4 | 172 | 108.7 | 175 | LSTM superior
The LSTM consistently beats baseline models, yielding lower MAE & RMSE, meaning more accurate 1‑hour ahead power forecasts.
LSTM has higher accuracy than other baseline models

## Slide 14: DashBoard
Showcasing now

## Slide 15: Thank you
CIVE70111 - Machine Learning
Group 11
12/12/2025